## Slide 1
Host Machine running
Ansible and Python Scripts
Terminal Console Servers
FTP Server
Router
TELNET
SSH
Console Link
Console Link
Connecting to Console Port
Transferring JunOS Code and Base Configs
ZTP Process

## Slide 2
Main Ansible Playbook
.yml
ZTP Process
bootstrap_initial.py
transfer_junos_file.py
junos_upgrade_re1.py
mastership_switchover.py
junos_upgrade_re0.py
bootstrap_ssh.py
load_baseconfig.py
Transfer Base config to Router
Future Plans:
Build a Web Page to invoke the script from
Will have facility to build the bootstrap config
PARAMIKO

## Slide 3
Initial Bootstrap Config
Transfer JunOS Code to both REs (internally copies to 2nd RE)
Upgrade Routing Engine-1
Switch the Mastership
Upgrade Routing Engine-0
Apply Secure Bootstrap Config including SSHv2
Transfer Base Config to Router
Load/Commit Base Config on Router
Connecting to Terminal Server and configuring
Transferring code over FTP
Sending SSH Configs and removing in-secure FTP and Telnet config
ZTP Process
Transferring over SCP
Config
verification
VERIFICATION STEPS
JunOS MD5
HASH Check
Version Check
Version & State
Check
Version Check
Config
verification
Config
verification
Can be combined into one step